The Optimal Configuration of Cogeneration Systems Based on Natural Gas: a Parallel Evolutionary Approach

MARCO CΙSAR GOLDBARG

Departamento de Informαtica e Matemαtica Aplicada

Universidade Federal do Rio Grande do Norte

Campus Universitαrio, Lagoa Nova, Natal, RN

BRAZIL

ELIZABETH FERREIRA GOUVΚA GOLDBARG

Departamento de Informαtica e Matemαtica Aplicada

Universidade Federal do Rio Grande do Norte

Campus Universitαrio, Lagoa Nova, Natal, RN

BRAZIL

FRANCISCO DANTAS DE MEDEIROS NETO

Departamento de Informαtica e Matemαtica Aplicada

Universidade Federal do Rio Grande do Norte

Campus Universitαrio, Lagoa Nova, Natal, RN

BRAZIL

Abstract: - This work investigates the problem of determining the configuration of a cogeneration system that uses natural gas as its primary source of energy, such that the cost of this solution is minimum. Two parallel evolutionary algorithms are presented to solve this problem. These algorithms are based on the memetic and on the transgenetic metaphors. The algorithms are compared and the work shows that the transgenetic approach presents better and faster results.

Key-Words: - cogeneration system, natural gas, evolutionary algorithm, memetic algorithm, transgenetic algorithm, parallel algorithm

1   Introduction

Cogeneration is the simultaneous production of electricity and thermal energy from a single energy source such as natural gas, although a variety of fuels can be used. The first cogeneration systems date back to the 1880s when steam was still the primary source of power in industry [6]. The design of cogeneration systems has changed significantly as a result of the requirement that utilities allow cogenerators to interconnect with the utility grid. Power can be used on-site or exported. The thermal energy can be used for heating, cooling or both. The cogeneration system can be of any size. The only fixed requirement is that it be economically viable using criteria established by the investor.

To define the set of components of a cogeneration system is a hard task. Besides several technical constraints, there are a number of possibilities to organize a viable configuration of a given cogeneration system to meet a given load. This paper presents and compares two evolutionary algorithms to determine the minimum cost feasible configuration of a cogeneration system. Section 2 presents the problem description and formulation. In sections 3 and 4 the memetic and the transgenetic parallel algorithms are described. Section 5 reports the results of a computational experiment that compared the performance of these algorithms applied to the cogeneration problem. Finally, section 6 presents some remarks and conclusions.

2   The Cogeneration System

A cogeneration system is a composite of several interconnected equipments that must meet certain technical specifications. The most usual parts of a cogeneration system are: motors, turbines (steam and gas), chillers, boilers and generators. A determinant factor for the choice of which of these components will compose the configuration of a certain cogeneration system is the final use of the energy. For instance, a system can be developed to deliver low-temperature refrigerants. In general, this type of system uses a generator associated with an engine. The outcome gases fire a chiller. Figure 1 shows a cogeneration system to produce cold. The fuel energy is first used to start a gas turbine (GT). The turbine drives a generator (G) while the exhaust gases are routed to a recovery generator (R) where they are used to fire an absorption chiller (A).

Fig.1: Cogeneration system to deliver cold

The objective of a cogeneration system conducts its design. The brazilian center of gas technology (CTGAS) defines five types of cogeneration cycles: the Combined Cycle, the Combined Cycle and Process Steam, the Compression and Electricity Cycle, the Drying Cycle and the Cold-Absorption Cycle. Table 1 shows the minimum composition of each on of these cycles. The columns GE, HR, ST, GT, CP, MT, CH correspond, respectively to the following equipments: generator, heat recover, steam turbine, gas turbine, compressor, motor and chiller. The decision associated with the optimization of a cogeneration system must still concerns the policies for meeting the end-user requirements and commercial factors regarding the equipments, such as guarantee, confidence, availability, etc.

Fig. 2: Scheme of a cogeneration system for cold              delivering

| CYCLE | Number of Equipments |
| --- | --- |
|  | GE | HR | ST | GT | CP | MT | CH |
| Combined | 1 | 1 | 1 | 2 |  |  |  |
| Combined / Steam | 1 | 1 | 1 | 2 |  |  |  |
| Compression / Electricity | 1 | 1 | 1 | 2 | 2 |  |  |
| Drying | 1 | 1 |  | 1 |  |  |  |
| Cold - Absortion | 1 |  |  |  |  | 1 | 1 |

Table 1: Equipments in each cycle

Figure 2 shows a scheme to implement the system represented in Figure 1, where there are three classes of equipments: chillers, generators and motors. Due to technical and commercial factors, the cogeneration system configuration can be specified with distinct equipments of each class. It is also usual that a system contains different subsystems and that these subsystems are composed of distinct equipments too. Often, a scheme like the one represented in Figure 2 is configured with three distinct equipments in each class.

The market offers a number of distinct items of each class of equipment. Thus, the optimization of a cogeneration system may require solving a combinatorial problem with a huge number of feasible configurations. The number of classes, subsystems and items in each class is an open variable. The factors concerning technical and commercial features can be associated in a variable that represents a unified cost. Therefore, given a cogeneration scheme, a version of the problem of determining the optimum configuration of a cogeneration system may be stated as the problem of choosing, among the available items of each class, subsets of equipments (with a fixed cardinality) to compose the system.

In mathematical terms, this optimization problem can be stated by the objective function

(1)

subjected to the constraints

(2)

(3)

(4)

where:

number of units type i belonging to class j.

minimum power required from the components of class j.

power supplied by component i of class j.

cost of one unit of component i of class j.

required amount of components of class j.

The constraints (2) assure that the equipments that compose the cogeneration system provide a minimum required power. The constraints (3) fix the number of equipments of each class in accordance to the configuration of the cogeneration system.

The following two sections present two evolutionary algorithms to solve this problem.

3   Memetic Algorithm - MA

Memetic Algorithms are evolutionary algorithms in which local search plays a significant role [8]. The general idea behind Memetic Algorithms is to combine the potential of Genetic Algorithms [3] with the power of local search as a tool to find good solutions quickly. A number of papers that report successful applications of Memetic Algorithms applied to optimization problems are listed in the work of Merz and Freisleben [5]. Figure 3 shows a general template of the Memetic Algorithm implemented in this work.

Fig. 3: Memetic algorithm in pseudo code.

Chromosome. The chromosomes that encode the solutions are structured according to the cogeneration cycle being modeled. Consider a Cold-Absorption Cycle with three equipments of each class. A solution to that configuration contains 3 equipments of each class and each class has a given cardinality. Figure 4 shows a chromosome that models a solution of the cogeneration cycle represented in Figure 1. The three classes of equipments are represented sequentially in the chromosome. The first three positions of the chromosome represent the components of class 1, generators, the next three positions represent the components of class 2, motors, and, finally the three positions represent the components of class 3, chillers. The alleles are the indices of the components of each class. The fitness of a chromosome is the total cost of the equipment.

Fig. 4: A chromosome for the cooling cycle

Population P. P is generated randomly. A computational experiment determined a size of 1000 individuals for P.

Subpopulation P’. The 10% best chromosomes and another 5% chosen at random compose the set of parents of the next generation.

Crossover. Two chromosomes generate one child. Recombination is done only between genes of the same class. The alleles of the parents that represent the cheapest equipments are copied to the offspring, provided that the minimum required power is met. If the fitness of the child is better than the fitness of, at least, one parent, then the child replaces the parent with the worst fitness in the population. The number of crossover operations in one iteration was determined with the aid of a computational experiment, being 7.5% of P.

Mutation. The mutation operator is a random pairwise interchange procedure. It chooses a component of the current solution and replaces it by another one that also provides the minimum required power. Thus, new components are selected at random until finding one that provides the minimum required power. The number of mutation operations was determined with the aid of a computational experiment, being 5% of P.

Local search. This procedure is a variant of the 2-swap heuristic. The neighborhood is defined as the set of solutions that can be reached from the current solution by exchanging a component of a given class with another of the same class.

A component of class j, j=1, …, m, is replaced by another one of the same class. To choose the component that will replace the other one, 30% of the available components are examined. The one that gives the best improvement to the chromosome fitness is chosen when the algorithm is being applied to an instance with n < 1000. For instances with n = 1000, due to the large runtimes needed to run these instances, the replacement is done when the first component that improves the chromosome fitness is found.

Parallel implementation. The parallel memetic algorithm was implemented in a master-slave architecture where each processor runs a copy of the algorithm. When the best solution in not improved during 250 iterations, then the master processor sends a message to the slaves asking for their better solution. If the best solution of the slaves is better than the master best solution, then the master sends it to the other slaves. The process stops when the best solution is not improved in the master processor for 2000 iterations.

4   Transgenetic Algorithm

As in Biology, Culture also exhibits evolution patterns [1]. Some researches show that genes and culture are inherently linked [4]. Memes can be thought of as units of information that are spread among the individuals of some culture [7]. The genes prescribe epigenetic rules, which are the regularities of the sensorial perception and mental development that motivate and direct culture acquisition. Culture helps to determine which prescriptive genes survive and multiply from one generation to the next. New well succeeded genes modify the epigenetic rules of the population. The modified epigenetic rules alter the direction and efficiency of the cultural acquisition channels giving feedback to the gene x meme co-evolution [9].

The epigenetic stage of a Memetic Algorithm is mainly expressed through local search procedures that are used to improve the chromosomes. Plotkin [7] defines memes as units of information that are encoded and transmitted by non-genetic means. This work adopts Plotkin’s definition of memes and considers that a meme is a unit of information originated in a non-genetic context used to reorganize a chromosome or a block of genes. Memetics is used in Computational Transgenetics to create a continuous process where memes are obtained and inserted in the genetic context. The computational agents that manipulate the chromosomes are similar to the intracellular vectors of Genetic Engineering. Their use allows the epigenetic rules be expressed in the evolutionary process.

The Computational Transgenetics is a multi-agent proposal based on three central ideas. The first idea is insert information in an evolutionary process to guide it. To accomplish this task, it is necessary to have a previous plan. Thus, the second idea is to plan the process of infiltration in the genetic context and to build agents in accordance to the epigenetic paradigm. In this stage, the ideas of memes and cultural evolution are incorporated to the process. Finally, the third idea is to use the prokaryotic recombination as a complimentary tool to preserve the genetic information. This allows minimizing the obstacles to transform memetic information in genetic information.

4.1     Transgenetic Agent

To insert the information in the genetic context, the transgenetic algorithms use transgenetic agents. A transgenetic agent consists of one or more memes and a manipulation method. The method of a transgenetic agent contains procedures (operators) to reorganize the code of the manipulated chromosome and other rules to evaluate the agent’s strategy. These rules can remodel the meme loaded on an agent and can guide the use of the operator or the use of memes. The transgenetic agents transport and transcribe information in the chromosomes of a given population. A transgenetic agent  is a pair (I, ) where I represents an information string that corresponds to given memes and  represents the agent’s manipulation method.  = (p1, …, ps) where pj, j = 1,…,s, are procedures that determine the behavior of an agent. A transgenetic agent is characterized by altering the configuration of a chromosome. Given a population P of size N, P={S1, S2,..., SN}, where a chromosome , i=1,..,N is an integer-valued string of length n representing a problem solution and fit a fitness function, such that , then . It means that the manipulation method  of an agent  transforms a chromosome Si in a chromosome Si’ according to I. As a consequence fit(Si) may also change. The procedures that can compose the manipulation method of an agent are:

- p1 - Attack, A. A: Si  {true, false}, i=1,…,N.. This procedure defines a criterion to determine whether a chromosome is sensitive to the manipulation of a given agent.

- p2 - Transcription Operator, . This procedure determines how an information string I is transcribed in a chromosome. An agent has only one transcription operator.

- p3 - Information Preservation, . This procedure determines for how long the information transcribed in a chromosome is preserved. This period of time can be defined as number of iterations, number of generations, etc.

- p4 - Transcribed Information Unblock, -1. This procedure resets the original behavior of a chromosome, that is, it ends the restrictions caused by a certain manipulation. Eventually, it must be necessary to restore certain original features of a manipulated chromosome, for instance, when an agent includes artificial material in a chromosome and it must be removed.

A transgenetic agent = (I, ) is called “virus” when s = 4 and is called Mobile Genetic Particle, when I is a DNA fragment and s = 2.

4.2     ProtoG Algorithm

Many algorithmic constructions can be supported by the transgenetic metaphor and are presented in [2]. This work presents one of them, a ProtoG algorithm. ProtoG algorithms are based on the prokaryotic cell model. It means that the evolutionary process of a ProtoG is developed on non-sexual basis. Furthermore, a chromosome alteration occurs only with the interference of an agent. Thus, these agents are the key of the evolutionary process in the ProtoG algorithms, being the unique sources for intensification and diversification of the search process. Figure 5 shows a general template of a ProtoG algorithm. At first the memetic and genetic contexts are created (meme base and chromosomes, respectively). Then, a transgenetic agent is formed with a meme and a method to transcribe the meme in the chromosomes. In the ProtoG version implemented in this work, a transgenetic agent attacks all the chromosomes in a given iteration. The transgenetic agents chosen to the implementation of this work are mobile genetic particles. In this work, the sensitiveness of a chromosome to an agent’s attack is related to its fitness. That is, a chromosome is sensitive to an agent if its fitness is improved after the manipulation. If the fitness of a chromosome is better than the current best fitness, then the chromosome shall transmit its memes to the others. Its memes update the meme base and new transgenetic agents can be created with this new set of information. In general, during the meme base update, new and promising memes replace old and not useful ones. This process is repeated until no new memes are generated during a fixed number of iterations.

Population. The chromosomes are encoded as in the memetic algorithm and the population is also generated at random.

Initialize a meme base, MB; Initialize a population, P; Repeat Generate a transgenetic agent, a; for each chromosome c of P do if c is sensitive to a’s manipulation then c := manipulation(a, c); if fitness(c) < best_current_fitness then include c’s memes in MB; end_if; end_for; until stop_criterion be satisfied;

Fig. 5: ProtoG algorithm in pseudo code.

Meme base. There are ten solutions in the meme base. Initially, the solutions of the meme base are obtained from a greedy heuristic that sorts the equipments of each class in a non-decreasing order of costs and then constructs viable configurations following this order. The meme base is updated when a new best solution is found. When it occurs the new solution replaces the worst solution in the meme base.

Transgenetic Agent. The mobile genetic particles were chosen to implement the transgenetic algorithm described in this work. The size of the transgenetic agents was determined experimentally, being two. To build the memes to be loaded in the transgenetic agents, a greedy heuristic was used to generate an initial solution. The greedy algorithm sorts the components of each class in a non-decreasing order of costs and chooses the first component that provides the minimum demand for power. Since, the length of a solution is 3m, where m is the number of classes of equipments of a cogeneration cycle, the greedy solution is partitioned in 3m/2 pieces. The partition is done at random, that is, two equipments are randomly chosen to form a meme. The piece with the lowest cost is chosen as the winner meme. Initially, the meme base contains only the greedy solution. When a new best solution is generated, it is included in the meme base. The meme base grows until reaches a size n/2, where n is the cardinality of the classes of equipments. When it happens, a new best solution updates the meme base replacing the worst solution. The transgenetic agent transcribes its information in a chromosome according to the improvement of the fitness. That is, if one or both equipments loaded in the mobile genetic particle improve the fitness of the chromosome and provide the minimum requirements of power, then this or these components of the mobile genetic particle replace randomly chosen components of the same class in the chromosome.

Parallel implementation. As for the memetic algorithm, ProtoG was implemented in a master-slave architecture where each processor runs a ProtoG algorithm. The same criterion for message passing and the same stop criterion are used.

5   Computational Experiments

The processors of the experiment are Pentium III 850 MHz, the master has 256 Mb of RAM and the others have 128 Mb of RAM. The algorithm was implemented in C++ with Message-Passing Interface in a Linux platform. The machines used in the implementation have 2, 4 and 8 processors.

Thirty-five instances were randomly generated with 100, 200, 300, 400, 500, 600 and 1000 as the fixed cardinality of the class of equipments. The instances are based on schemes with three components of each class. The power and the costs of the equipments were randomly generated according to a uniform distribution in the following ranges: motors – [110,330] HP, chillers – [15000,40000] BTU, generators – [5,15] MW, turbines – [105,600] MW, boilers – [50,150] MW and costs – [400,1200] monetary units.

Ten independent runs were performed for each instance. The relative behavior of the algorithms was very similar for the five cycles both in terms of quality of the solution found and runtime. Thus, this work presents the relative behavior of the algorithms for the Compression/Electricity cycle. Figure 6 presents the minimum, average and maximum gap between the best solution found by the algorithms ProtoG and MA for 2, 4 and 8 processors. The graphic shows that ProtoG is slightly better than the MA for 2 processors, however this difference increases significantly for 4 and 8 processors. Figure 7 shows the average gap between the runtime. The gap, in both cases, were computed by ((MA_result – ProtoG_result)/ProtoG_result)*100. ProtoG runtime is significantly better than the MA for all the orders (number of equipments) of the cogeneration instances.

Fig. 6: Solution quality gaps.

6 Conclusion

The experiments showed that the transgenetic algorithm behaved significantly better than the memetic algorithm, finding better solutions and being faster. This difference increases with n and with the cycle under consideration.

Fig. 7: Runtime gaps.

References:

[1] Boyd, R., and P. Richerson, Culture and Theory of Social Evolution, Sage Publications, London, 1985.

[2] Goldbarg, M. C., and E. F. G. Goldbarg, Transgenιtica Computacional: Uma aplicaηγo ao Problema Quadrαtico de Alocaηγo, Pesquisa Operacional, Vol. 22, No 3, 2002, pp. 359-386.

[3] Holland, J. H., Adaptation in Natural and Artificial Systems, University of  Michigan Press, Ann Arbor, MI, 1975.

[4] Lumsden, C. J., and E. O. Wilson, 1981, Genes, Mind and Culture, Harvard University Press, Cambridge.

[5] Merz, P. and B. Freisleben, Fitness Landscape Analysis and Memetic Algorithms for the Quadratic Assignment Problem, IEEE Transactions on Evolutionary Computation, Vol. 4, No 4, 2000, pp. 337-352.

[6] Orlando, J. A., Cogeneration Design Guide,  American Society of Heating, Refrigerating and Air-Conditioning Engineers, New York, 1997.

[7] Plotkin, H. C., Non-genetic Transmission of Information: Candidate Cognitive Processes and the Evolution of Culture, Behavioural Processes Vol. 35, 1996,  pp. 207-213.

[8] Radcliffe, N. J. and P. D. Surry, Formal Memetic Algorithms, Evolutionary Computing, Lecture Notes in Computer Science Vol. 865, Springer Verlag, Berlin, 1994, pp. 1-16.

[9] Wilson, E. O., Consilience, A. A. Knopfs (Ed.), New York, USA, 1998.